Battery Guide

REF:	https://www.youtube.com/watch?v=saxYilLJ7yw

LiPo/ Lithium Polymer
LiFWPO4/ Lithium
SLA/ Sealed Lead Acid
Ni-Cds/ Nickel Cadmium
Ni-MH/ Nickel Metal Hydride
# LiPo/ Lithium Polymer
- Highest energy density
- Costliest
- Special circuit for safety –
  - Overcharge –
    - never charge above 4.2V per cell. Else it can xplode
    - requirs good charrging circuit , Under charge below 3V, Puffy battery,
  - Discharge
    - if the LiPo battery is discharged below 3V/Cell it can permanently loose some capacity
  - Puffy battery
  - Can get heated up so should constantly monitor temperature
  - Applications	-	Phone, laptops, light weight devices etc.

# LiFePO4/ Lithium Iron Posphate
- High capacity after LiPo
- No explosions like LiPo
- Charging and discharging circuits required but inappropriate use will cause only loosing some battery capacity
- Little heavier than Lipo
- Applications	-	Light weight robotic, power tools, RC toys etc.

# SLA/ Sealed Lead Acid
- Lot durable than Li (Lithium) batteries
- Better cope with accidental overcharges or discharges
- Best value for money
- Handles extreme temperatures
- Heavy and bulky
- Applications	-	Cars, motorcycles, solar energy storage, emergency power supply etc.

# Ni-Cds/ Nickel Cadmium
- Cheap
- Lasts longer than SLA
- Memory effect – Needs to be regularly fully discharged and then fully recharge to maintain high capacity

# Ni-MH/ Nickel Metal Hydride
- Higher capacity than Ni-Cd
- Very high self discharge rate. May discharge without using after around 2 months. If needs to use ones with low self discharging needs to be selected. e.g Eneloop
- Cheaper in long run than using Alkaline batteries
- Little expensive than Ni-Cds
- No memory effect
- Bigger and heavier than Lithium (Li) batteries
- Very safe to work with
- Applications	-	Consumer rechargable batteries